## Slide 1: Multiserver Queue simulation (M/M/c)
Hashim Al-Sadah
Abdulwahab Alghamdi
Hussain Alsinan

## Slide 2: Objective
To simulate and evaluate M/M/c queueing system with an infinite buffer.
To obtain the empirical PMF for and the PDF for the total time in the system and waiting time.
To obtain and from simulation.
To study the affect of increasing the number of servers on the probability of having to wait
All the empirical results are compared with the theoretical ones.

## Slide 3: State Diagram
is the number of servers.
is the arrival rate.
is the rate of serving for one server.
is the traffic intensity.

## Slide 4: Simulation Code
Initial parameters needed:
  Lambda (λ), Mue (µ), Number of servers (c) and number of customers.
  For system stability,
The system has a Poisson arrival process and an exponential service rate.
Arrival Times occur at a rate of
Service Times occur exponentially at a rate of
The simulation code will therefore calculate departure times for a multiserver queue system.

## Slide 5: Main Simulation Loop (Finding Departure Times)
Find the server with the earliest available time.
Assign the corresponding minimum index to the earliest available time.
Calculate start time:
  If AT(i) > earliest available time, it means the server was idle for some time and the start time will be AT(i).
  If earliest available time > AT(i) it means the customer had to wait and the start time will be earliest available time.
  Startlist will be updated.
Calculate departure time:
  Departure time will be the start time + service time.
  DT will be updated.
serverList which is the latest departure for every server will be updated.
ServiceTime which is the total service time for every server will be updated be adding the latest service time with total service time.

## Slide 6: Main Simulation Loop (Finding Departure Times)
Customer Arrival
Find earliest available server
AT > Earliest
Capture Arrival Time
Server is idle, AT=startTime
Server is busy, Earliest =startTime
AT < Earliest
DT = startTime+ ST
serverList Updated with DT
Iteratively for N Number of Customers

## Slide 7: Example
serverList <0,0>
serverTime <0,0>
earliestAvailableTime = 0
startTime =0
departureTime = 0
AT | 2 | 3 | 4 | 7 | 11 | 18
ST | 1 | 3 | 5 | 1 | 2 | 6
startTime |  |  |  |  |  | 
DT |  |  |  |  |  | 
serverID |  |  |  |  |  | 

## Slide 8: Example
serverList <3,0>
serverTime <1,0>
earliestAvailableTime = 0
startTime =2
departureTime = 3
AT | 2 | 3 | 4 | 7 | 11 | 18
ST | 1 | 3 | 5 | 1 | 2 | 6
startTime | 2 |  |  |  |  | 
DT | 3 |  |  |  |  | 
serverID | 1 |  |  |  |  | 

## Slide 9: Example
serverList <3,6>
serverTime <1,3>
earliestAvailableTime = 3
startTime =4
departureTime = 9
AT | 2 | 3 | 4 | 7 | 11 | 18
ST | 1 | 3 | 5 | 1 | 2 | 6
startTime | 2 | 3 | 4 |  |  | 
DT | 3 | 6 | 9 |  |  | 
serverID | 1 | 2 | 1 |  |  | 

## Slide 10: Example
serverList <9,6>
serverTime <6,3>
earliestAvailableTime = 6
startTime =7
departureTime = 8
AT | 2 | 3 | 4 | 7 | 11 | 18
ST | 1 | 3 | 5 | 1 | 2 | 6
startTime | 2 | 3 | 4 | 7 |  | 
DT | 3 | 6 | 9 | 8 |  | 
serverID | 1 | 2 | 1 | 2 |  | 

## Slide 11: Example
serverList <9,8>
serverTime <6,4>
earliestAvailableTime = 8
startTime =11
departureTime = 13
AT | 2 | 3 | 4 | 7 | 11 | 18
ST | 1 | 3 | 5 | 1 | 2 | 6
startTime | 2 | 3 | 4 | 7 | 11 | 
DT | 3 | 6 | 9 | 8 | 13 | 
serverID | 1 | 2 | 1 | 2 | 2 | 

## Slide 12: Example
serverList <9,13>
serverTime <6,6>
earliestAvailableTime = 9
startTime =18
departureTime = 24
AT | 2 | 3 | 4 | 7 | 11 | 18
ST | 1 | 3 | 5 | 1 | 2 | 6
startTime | 2 | 3 | 4 | 7 | 11 | 18
DT | 3 | 6 | 9 | 8 | 13 | 24
serverID | 1 | 2 | 1 | 2 | 2 | 1

## Slide 13: Example
serverList <24,13>
serverTime <12,6>
earliestAvailableTime = 13
startTime =18
departureTime = 30
AT | 2 | 3 | 4 | 7 | 11 | 18 | 20
ST | 1 | 3 | 5 | 1 | 2 | 6 | 10
startTime | 2 | 3 | 4 | 7 | 11 | 18 | 20
DT | 3 | 6 | 9 | 8 | 13 | 24 | 30
serverID | 1 | 2 | 1 | 2 | 2 | 1 | 2

## Slide 14: Tracking N and AUC
Event (clock)
Arrival
Departure
N+1
Calculate AUC
Calculate AUC
N-1
if AT(i) < DT(j)
if AT(i) > DT(j)

## Slide 15: Results

## Slide 16: Results

## Slide 17: Results (total time PDF)

## Slide 18: Results (total time PDF)

## Slide 19: Results (total time PDF)

## Slide 20: Results (total time PDF)

## Slide 21: Results (total time PDF)

## Slide 22: Results (total time PDF)

## Slide 23: Results (waiting time PDF)

## Slide 24: Results (waiting time PDF)

## Slide 25: Results (waiting time PDF)

## Slide 26: Results (waiting time PDF)

## Slide 27: Results (waiting time PDF)

## Slide 28: Results (no of Customers PMF)

## Slide 29: Results (no of Customers PMF)

## Slide 30: Results (no of Customers PMF)

## Slide 31: Results (no of Customers PMF)

## Slide 32: Results (no of Customers PMF)

## Slide 33: Results (waiting probability)

## Slide 34: Conclusion
The results of the simulation are showing an excellent agreement with theoretical results, which indicates that the simulation code is working properly.